## Slide 1
Vietnam Power Sector Reform
And Market Development
Pham Manh Thang – Member of EVN Board of Director
Vietnam Power Sector Reform
And Market Devvelopmentvvvv
VIETNAM POWER SECTOR REFORM
AND COMPETITIVE MARKET DEVELOPMENT
PHAM MANH THANG – Member of Board of Director
Notes: 1

## Slide 2
Contents
2. Electricity Reform Roadmap
3. Power Market Design and Operation
1. Overview of Vietnam Energy Sector
4. Lesson Learned
Notes: 2

## Slide 3
Overview of Vietnam Energy Sector
Notes: 3

## Slide 4
Overview of Vietnam Energy Sector
1. Potential Primary sources:
Vietnam: a South East Asia country; area of 331,210 km2; population of 95 million; and per capita income of 2500 USD (as of 2018).
Commercial potential of primary energy sources | 
Coal | 3.5 billion tones (33.4 million tone are used in 2017)
Natural Gas | 270 billion m3 (6 billion m3 are used in 2017)
Hydro | 110 billion kWh/year, (86.6 billion kWh in 2017)
Wind | 7.200 MW
Solar | 8.000 - 40.000 MW
Geothermal | 680 MW
Notes: 4

## Slide 5
Overview of Vietnam Energy Sector
2. Generation mix:
Installed capacity by 10/2018 | MW | %
Hydro | 19,674 | 40.25
Coal-fired | 18,430 | 37.7
Gas-fired | 7.528 | 15.4
Oil-fired | 1,500 | 3.1
Import | 1,340 | 2.75
Renewable | 403 | 0.8
Total | 48,875 | 
Network | Unit | Quantity
500 kV transmission line | Km | 7,444
200 kV transmission line | Km | 16,551
110 kV distribution line | Km | 20,215
Medium and low voltage line (2015) | Km | 476,572
500 kV substation | MVA | 26,100
220 kV substation | MVA | 44,602
110 kV substation | MVA | 50,813
Medium and low voltage substation | MVA | 81,141
Losses: 7.24% in 2017
Notes: 5

## Slide 6
Overview of Vietnam Energy Sector
2. Generation mix (cont.)
Chart: 2015 38537 MW
| Hydro | Coal - fired | Gas turbine and Oil - fired | Small HPP + Renewable Energy | Import
 | 15258 | 12717 | 8478 | 889 | 1195
Chart: 2020 59779 MW
| Hydro | Coal - fired | Gas turbine and Oil - fired | Small HPP + Renewable Energy | Nuclear | Import
 | 18161 | 26712 | 9466 | 4004 | 1436
Chart: 2025 89074MW
| Hydro | Coal - fired | Gas turbine and Oil - fired | Small HPP + Renewable Energy | Nuclear | Import
 | 18531 | 45265 | 16783 | 7059 | 1436
Chart: 2030 112836 MW
| Hydro | Coal - fired | Gas turbine and Oil - fired | Small HPP + Renewable Energy | Nuclear | Import
 | 21191 | 59375 | 18913 | 11849 | 4600 | 1508
- VN power system is second largest system in Southeast Asia, 29th in the world
- 99% of Vietnamese citizens have access to electricity
Notes: 6

## Slide 7
Power Sector Reform
Notes: 7

## Slide 8
Power Sector Reform
1. Motivations for Power Sector Reform:
To adapt to the transition from central planning economy to opened market economy and globalization process.
To introduce competition into power sector in order to increase efficiency and transparency in business and finally to have reasonable tariff to the end-users.
To form a market platform to attract investment in generation in order to meet a constant high growth rate of demand (more than 14% per year during period 1995-2005).
To have long term sustainable development of the industry (affordable price; environment issue; market signal for supplying side and demand side; government debt…etc).
Notes: 8

## Slide 9
Stage 1
Stage 2
Stage 3
Competitive Generation market
(VCGM)
Trial run: 2011-2012
Official operation: 2012-2018
Competitive Wholesale market
(VWEM)
Trial run : 2017-2018
Official operation: 2019-2021
Competitive Retail market
(VREM)
Trial run: 2021-2023
Official operation: 2023
2. The Electricity Market Development Roadmap:
Power Sector Reform
Notes: 9

## Slide 10
2008
2009
2012
2016- 2020
2006
Roadmap for electricity competitive market development issued by PM
2004
Electricity law passed by Parliament
National Power Transmission Corporation (NPT) establishment
Competitive generation market design approval, Mechanism for adjustment of market retail tariff isued
Establishment of 3 Gencos
Competitive generation market officially in operation
Starting Equitization process (Genco 3 is equitized in 2017)
Network operation and retail in power distribution companies are separated
Distribution companies become buyers in wholesale power market
EVN is asigned to be the single buyer for generation power market
Electricity Regulatory Authority of VN (Regulator) establishment
3. Power Sector Reform Implementation:
Power Sector Reform
Notes: 10

## Slide 11
Power Sector Reform
4. VCGM Structure:
Notes: 11

## Slide 12
Power Sector Reform
 | Common market design | VCGM
Market model | Cost based or price based | Cost based; energy payment and capacity payment (CAN)
 | Net pool or gross pool | Gross pool and vesting contracts.
 | Single Buyer, Wholesale and Retail market | Single Buyer
Price setting method | Node pricing or uniform pricing | Uniform pricing and constrains on payment
 | Ex-ant or ex-post | Ex-post
 | Pay as bid or marginal pricing | Marginal pricing. Determined based on price of last MW that meets the demand requirement.
Market structure | MSO or SO and MO | MSO – integrated structure
5. VCGM Design:
Notes: 12

## Slide 13
Power Sector Reform
Number pairs of quantity block/price | 5 bidding quantities along with 5 bidding prices.
Energy market | Day ahead market
Payment feature | 2 components: CfD contract and market payment.
Full market price setting | Equal to CAN (Capacity Add-on) + SMP price.
CAN setting | Determined and fixed for each hour for 1 year ahead. CAN is shortfall revenue of Best New Entrant.
Trading interval | 1 hour
Unit bid floor/cap | Every generating unit has bid floor/cap.
5. VCGM Design (cont.):
Notes: 13

## Slide 14
Power Sector Reform
6. VWEM Design:
a. VWEM design is mostly based on VCGM design in term of spot market with flowing improvements:
(i) transit from single buyer to multibuyers.
(ii) Step by step moving from the cost based model to the price based model without CAN payment mechanism.
(iii) Step by step shortening trading interval from 1hour to 15 minutes when the market information system available.
b. In term of contracting framework:
(i) CfD contract directly between market generators and PCs;
(ii) Allocating existing PPAs from EVN to 5 others PCs.
Notes: 14

## Slide 15
Power Sector Reform
Chart: Number of Power Plants in VCGM from 2012 to 2018
| 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018
Total | 80 | 93 | 100 | 108 | 114 | 128 | 132
Direct | 28 | 43 | 51 | 60 | 71 | 81 | 87
Indirect | 11 | 11 | 12 | 14 | 15 | 18 | 22
Temporarily Indirect | 27 | 24 | 21 | 16 | 10 | 11 | 4
SMHP | 11 | 12 | 12 | 14 | 14 | 14 | 14
BOT | 3 | 3 | 4 | 4 | 4 | 4 | 5
7. VCGM Results:
Notes: 15

## Slide 16
Power Sector Reform
SMP and FMP (SMP+CAN) prices
SMP
FMP
7. VCGM Results (cont.):
1 USD ≈ 22000 VND
Notes: 16

## Slide 17
Lesson Learned
Notes: 17

## Slide 18
Lesson Learned
Legal framework: Power market development should be carried out in parallel with power sector reform (In Vietnam, power sector reform is approved and issued nearly every 5 years while power market development road map is approved for all stages of 20 years).
Retail tariff adjustment mechanism and primary energy market should be introduced in conjunction with power sector reform and power market development (In Vietnam, domestic coal, natural gas price and uniform retail are regulated by Government)
An electricity regulatory body should be established robustly and independently from state management agencies.
A big power system with high demand growth rate of more 10% will require huge of capital to invest in generation. Hence, the market design should be cost-based first.
Notes: 18

## Slide 19
Lesson Learned
Vietnam is currently lacking of primary energy markets, so transparency of fuel prices for power generation in power market environment is an big issue. A mechanism to put into operation of coal, oil and gas into energy market to ensure that the transactions on primary energy are fair, transparent and competitive.
Electricity retail tariff is uniform throughout the country, not reflecting the supply demand equilibrium. In near future, it is necessary to implement the mechanism of having retail electricity prices by regions.
Notes: 19

## Slide 20
Thank you!
Vietnam Electricity
Address: 11 Cua Bac, Ba Dinh, Hanoi, Vietnam
Tel: (84-4) 6.6946789 - Fax: (84-4)6.6946666
Notes: 20